### 1. NSA (Non-Standalone) Call Flow
NSA leverages existing LTE infrastructure (eNodeBs) for control signaling and uses 5G NR (New Radio) for user plane data. Here's how the call flow generally works in NSA:
#### UE Initialization and Attach Procedure
1. Attach Request:
  1. The UE sends an Attach Request to the LTE eNodeB.
2. eNodeB to MME:
  1. The eNodeB forwards this request to the MME (Mobility Management Entity).
3. Attach Accept:
  1. The MME processes the request and sends an Attach Accept to the eNodeB, which forwards it to the UE.
4. Attach Complete:
  1. The UE responds with an Attach Complete message.
#### Session Establishment Procedure
1. Initial Context Setup Request:
  1. The MME sends an Initial Context Setup Request to the eNodeB to establish bearer contexts.
2. Bearer Resource Setup:
  1. The eNodeB sets up the bearer contexts and responds with an Initial Context Setup Response.
3. Bearer Resource Command:
  1. The MME may send a Bearer Resource Command to configure bearers.
4. Bearer Resource Setup Response:
  1. The eNodeB responds with a Bearer Resource Setup Response.
#### 5G NR Connection Setup
1. NR Cell Selection:
  1. The UE selects a 5G NR cell and sends an RRC Connection Request to the gNodeB.
2. gNodeB to AMF:
  1. The gNodeB forwards this request to the AMF (Access and Mobility Management Function).
3. N2 Setup Request/Response:
  1. The AMF and gNodeB exchange N2 Setup Request and N2 Setup Response to establish the N2 interface.
4. RRC Connection Setup:
  1. The gNodeB sends an RRC Connection Setup message to the UE, which responds with an RRC Connection Setup Complete.
#### Bearer Setup in 5G
1. Bearer Resource Command:
  1. The AMF sends a Bearer Resource Command to the gNodeB to set up 5G NR bearers.
2. Bearer Resource Setup Response:
  1. The gNodeB responds with a Bearer Resource Setup Response.
#### Call Establishment and Management
1. Call Setup:
  1. The call setup involves coordination between LTE and 5G NR bearers.
2. Handover and Mobility:
  1. The handover procedure involves both LTE and 5G components if the UE moves between cells or networks.
3. Call Release:
  1. The call release involves deactivating bearers and terminating the call.
### 2. SA (Standalone) Call Flow
SA uses a complete 5G architecture, including 5G core (5GC) and 5G NR, without relying on LTE infrastructure. Here’s how the call flow generally works in SA:
#### UE Initialization and Attach Procedure
1. Attach Request:
  1. The UE sends an Initial UE Message to the 5G gNodeB (NR cell).
2. gNodeB to AMF:
  1. The gNodeB forwards this to the AMF via the N2 interface.
3. Registration Request:
  1. The AMF processes the registration request and responds with a Registration Accept.
4. Registration Complete:
  1. The UE responds with a Registration Complete.
#### Session Establishment Procedure
1. Session Request:
  1. The AMF sends a Session Establishment Request to the SMF (Session Management Function).
2. Session Response:
  1. The SMF processes the request and sends a Session Establishment Response back to the AMF.
3. Bearer Resource Command:
  1. The AMF sends a Bearer Resource Command to the gNodeB to set up bearers.
4. Bearer Resource Setup Response:
  1. The gNodeB responds with a Bearer Resource Setup Response.
#### Call Establishment and Management
1. Call Setup:
  1. In SA, the call setup is handled entirely through 5G protocols, including interactions between gNodeB, AMF, and SMF.
2. Handover and Mobility:
  1. Handover procedures are handled within the 5G system, utilizing the 5G core network for mobility management.
3. Call Release:
  1. The call release procedure involves deactivating bearers and terminating the call entirely within the 5G ecosystem.
### Summary of Differences
- Control Signaling:
  - NSA: Uses LTE (eNodeB and MME) for control signaling and 5G NR for data.
  - SA: Uses 5G core (AMF and SMF) and 5G NR for both control signaling and data.
- Architecture:
  - NSA: Hybrid architecture, combining LTE and 5G components.
  - SA: Fully 5G architecture, with complete reliance on 5G core components.
- Bearer Management:
  - NSA: Manages bearers using both LTE and 5G protocols.
  - SA: Manages bearers entirely through 5G protocols.
- Handover:
  - NSA: Handover involves both LTE and 5G NR components.
  - SA: Handover is managed within the 5G ecosystem.