GUAMI stands for Globally Unique AMF Identifier. It is a crucial component in the 5G core network architecture used to uniquely identify an AMF (Access and Mobility Management Function) instance across the entire network.

PLMN is a unique identifier for a mobile network operator’s network and is used to distinguish between different mobile networks.

TAI is used to identify a tracking area in the network, which is a geographical area where the mobile network tracks the user's location. The TAI helps in managing mobility and location updates efficiently.

 This configuration file is for an AMF (Access and Mobility Management Function) component in Open5GS, which is part of a 5G core network. Here's a step-by-step explanation of each section:
### 1. Logger Configuration
yaml
Copy code
logger:
  file:
    path: /var/log/open5gs/amf.log
    level: debug # fatal|error|warn|info(default)|debug|trace
- path: Specifies the file path where the AMF logs will be saved (/var/log/open5gs/amf.log).
- level: Sets the logging level for the AMF. Here, debug is specified, which means detailed debugging information will be logged. Other levels include fatal, error, warn, info (default), and trace.
### 2. Global Settings
yaml
Copy code
global:
  max:
    ue: 1024 # The number of UE can be increased depending on memory size.
# peer: 64
- max.ue: Defines the maximum number of User Equipments (UEs) that the AMF can handle. Here, it is set to 1024. This number can be increased based on available memory.
- peer: (commented out) If included, this would define the maximum number of peers (other network functions) the AMF can handle.
### 3. AMF Configuration
yaml
Copy code
amf:
  sbi:
    server:
      - address: 127.0.0.5
        port: 7777
    client:
# nrf:
# - uri: http://127.0.0.10:7777
      scp:
        - uri: http://127.0.0.200:7777
  ngap:
    server:
      - address: 127.0.0.5
  metrics:
    server:
      - address: 127.0.0.5
        port: 9090
  guami:
    - plmn_id:
        mcc: 999
        mnc: 70
      amf_id:
        region: 2
        set: 1
  tai:
    - plmn_id:
        mcc: 999
        mnc: 70
      tac: 1
  plmn_support:
    - plmn_id:
        mcc: 999
        mnc: 70
      s_nssai:
        - sst: 1
  security:
    integrity_order : [ NIA2, NIA1, NIA0 ]
    ciphering_order : [ NEA0, NEA1, NEA2 ]
  network_name:
    full: Open5GS
    short: Next
  amf_name: open5gs-amf0
  time:
# t3502:
# value: 720 # 12 minutes * 60 = 720 seconds
    t3512:
      value: 540 # 9 minutes * 60 = 540 seconds
- sbi (Service-Based Interface):
  - server: Defines the IP address and port where the AMF’s SBI server listens. Here, it is set to 127.0.0.5 on port 7777.
  - client: Configuration for connecting to other network functions.
    - scp: Service Communication Proxy (SCP) URI where the AMF connects (http://127.0.0.200:7777).
    - nrf: (commented out) Network Repository Function (NRF) URI, which is used if the AMF needs to connect to an NRF.
- ngap (Next Generation Application Protocol):
  - server: Defines the IP address where the AMF’s NGAP server listens, set to 127.0.0.5.
- metrics:
  - server: Defines the IP address and port for exposing metrics (performance data). Here, it’s 127.0.0.5 on port 9090.
- guami (Globally Unique AMF Identifier):
  - plmn_id: Identifies the network using MCC (999) and MNC (70).
  - amf_id: Identifies the AMF instance within the network, with region set to 2 and set to 1.
- tai (Tracking Area Identifier):
  - plmn_id: Identifies the network using MCC (999) and MNC (70).
  - tac: Tracking Area Code, 1, identifies a specific tracking area within the network.
- plmn_support:
  - plmn_id: Identifies the supported network using MCC (999) and MNC (70).
  - s_nssai: Single Network Slice Selection Assistance Information (S-NSSAI) with sst (Slice/Service Type) set to 1.
- security:
  - integrity_order: Specifies the order of integrity protection algorithms used (NIA2, NIA1, NIA0).
  - ciphering_order: Specifies the order of encryption algorithms used (NEA0, NEA1, NEA2).
- network_name:
  - full: The full name of the network (Open5GS).
  - short: The short name of the network (Next).
- amf_name: The name of the AMF instance (open5gs-amf0).
- time:
  - t3512: Timer value set to 540 seconds (9 minutes). This timer controls specific operations within the AMF.
The configuration defines how the AMF interacts with other network components, handles user sessions, manages security, and tracks user location. It ensures proper setup and functioning of the AMF within the Open5GS network.